STATICS OF A PARTICLE

RESULTANT FORCES

Example

Two forces of 3N and 4N act an angle of 90° to each other.

Find the magnitude of their resultant and the angle that it makes with the 4N force.

RESULTANT FORCES USING COMPONENTS

Example

Find the magnitude of the resultant force.

To find the total effect of a force in a particular direction, we resolve forces in that direction.

To indicate resolving forces horizontally, write  R(→)

To indicate resolving forces vertically, write R(↑)

McEx4A & 4B

EQUILIBRIUM OF COPLANAR FORCES

Forces are in equilibrium if there is no resultant force in any direction.  Forces must balance each other out.

Example

Example

A particle is in equilibrium at O under the action of forces X, Y and R as shown in the diagram.  Find the magnitude of R and the angle θ when X = 8N and Y = 6N

Ex 4A p 95

SPECIAL CASE – LAMI’S THEOREM

For 3 forces in equilibrium:

Proof

The 3 forces can be represented by a vector triangle:

Example

McEx4C

PROBLEMS INVOLVING SPECIFIC FORCES

Example

A particle of mass 3kg rests on a rough plane inclined at 30° to the horizontal.  It is held in equilibrium by a force of 12N acting up the plane at 10° to the plane.  If it is on the point of slipping down the plane, find the friction force.

Ex 4B p 101

EQUILIBRIUM INVOLVING FRICTION

Example

A body of mass 8kg is on an inclined plane of 45°.  It is held I place by a horizontal force of 20N and is about to slip down the plane. Calculate μ.

Ex 4C p 109

Mixed Ex 4D p 111

# Text boxes

Square and add to find R.  Divide to find θ